## Slide 1
SAI Specification for Chained ACLs

## Slide 2
ACL Stages in SAI Pipeline
Allows 4 stages in the pipeline
Each stage is chained i.e., output from one stage can be used as an input to later stage.
Each stage allows only single table group
Each stage allows sequential or parallel lookup within the table group members
Table group members can be an arbitrary combination of Exact Match or Ternary types.
Pre-Ingress
Table Group
Ingress
Table Group
Post-Ingress
Table Group
MACSec
Table Group
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Member
Member
Member
Member

## Slide 3
Shortcomings
Pre-Ingress
Table Group
Ingress
Table Group
Post-Ingress
Table Group
MACSec
Table Group
Do not allow chaining of tables within a [stage, group]
  How many such tables HW
  What grouping and order of tables
  Type of lookup in each such chain group
Why is it needed
  Newer HW support multiple HW blocks at one stage for scaling reasons
  Each block can be of TERNARY or EM type for cost reasons
  Each block MAY feed metadata to subsequent block for optimization reasons
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Table
Parallel Lookup
Sequential Lookup
Table
Table
Table
Table

## Slide 4
Proposal: Introduce Concept of Chain Group
What is Chain group
  New object that can be pointed by one or more table group members of a Table Group
  Lookup within the chain group object can be parallel or sequential
  Lookup across chain groups for a given ACL stage is cascaded aka chained.
  One chain group can feed metadata to subsequent chain group within an ACL stage or to the subsequent ACL stage

## Slide 5
Proposal: Introduce Concept of Chain Group
Table Group
<Ingress-Stage>
Table 1
Table 2
Table 3
Table 4
Member
Member
Member
Member
Chain Group 1 Stage 1
Chain Group 2 Stage 2
SAI Object View
HW Physical Table View
Table 3
Table 4
Table 1
Table 2
Parallel or Sequential Lookup
EM or Ternary
Parallel or Sequential Lookup
EM or Ternary
Chained Lookup
Lookup precedence when chain groups are configured

## Slide 6
SAI Spec Changes
New Chained Table Group Object
  SAI_OBJECT_TYPE_CHAINED_ACL_TABLE_CHAIN_GROUP
Chain group attribute to specify the order of chain group in the chain
ACL table group member points to a chain group
Lookup across the chain group for a given ACL stage is ALWAYS cascaded aka chained

## Slide 7
No change in the ACL Table Group binding to bind point like port/lag/rif etc
No change in existing ACL tables
No new bind point
Supports warm boot
Capability query for platforms not supporting chain groups
Backward Compatibility

## Slide 8
Query Platform Support:
sai_query_attribute_capability(switch_id, SAI_OBJECT_TYPE_ACL_TABLE_CHAIN_GROUP, SAI_ACL_TABLE_GROUP_MEMBER_ATTR_ACL_TABLE_CHAIN_GROUP_ID, attr_cap)
Query number of chain groups and their types
sai_acl_capability_t is enhanced to query for number of stages supported
  { . . .
  /**
  * @brief Number of chained stages and types supported for a given ACL stage.
  */
  sai_acl_chain_list_t acl_chain_list;
  } sai_acl_capability_t;
Capability Query
CRM for Table Chain Group count

## Slide 9
No previous ACL configuration is present
Step 0:
sai_query_attribute_capability() to check if device supports ACL chained table groups at ingress stage (as an example)
Query sai_acl_chain_list_t to check number of chain stages and type (EM or TERNARY) at each chain stage.
Step 1:
Create an ingress stage ACL Group
Create an ACL Table for EM or TERNARY match type
  Create an ACL Table entry
Create an ACL Chained group
  Set the lookup type for this chain group as Parallel or Sequential
  Set the chain group type as EM or TERNARY
  Set the chain stage
Step 2:
Create an ACL Table member
Point to ACL Group created in Step 1.1
Point to ACL Table created in Step 1.2
Point to ACL Chained group created in Step 1.3
Step 3:
1. Bind the ACL Group to a port/rif etc.
Workflow 1

## Slide 10
There exists a previous ACL Table group
Table Group: TG1, Parallel Lookup
Table T1: Ternary
Table T2: Ternary
New tables need to be added with parallel lookup.
Table T3: EM
Table T4: EM
Final Configuration should be:
Table Group: TG1
Chain Group: CG1 -> [T3, T4], Stage 0
Chain Group: CG2 -> [T1, T2], Stage 1
CG2 EM parallel lookup is after CG1 TERNARY parallel lookup
Workflow 2: Warm-boot Scenario
Table 1
Table 2
Table 3
Table 4
Stage 0
Parallel Lookup
EM
Stage 1
Parallel Lookup
Ternary
Chained Lookup

## Slide 11
Step 1:
Create an ACL Chained group CG2 for stage 1
  Set the lookup type for this group as Parallel
  Set TERNARY type
  Set the chain stage as stage 1
No traffic disruption and no change in policy for TG1, CG2 [T3, T4]
Create an ACL Chained group CG1 for stage 0
  Set the lookup type for this group as Parallel
  Set EM type
  Set the chain stage as stage 0
Create Tables T3, T4
Create Table group member TGM for T3 and T4
TGM3 and TGM 4 point to TG1 and CG1
Add T3 and T4 ACL entries
Pipeline is ready with the TG1, CG1 [T1, T2] policy
Step 2:
Update ACL table group member T1 to point to Chain group CG2 - No traffic Impact
Update ACL table group member T2 to point to Chain group CG2 – No traffic impact
Create ACL table group member T3 and point to Chain group CG1 – New Config
Create ACL table group member T4 and point to Chain group CG1. New Config
Bind point of table group TG1 is never changed.
Workflow 2

## Slide 12: SAI Header Release 1.12
Adaptive Routing and Switching (#1681)
Hierarchical ecmp (#1555)
SRV6 encap support to BFD (#1759)
SRv6 VPN enhancements (#1744)
ACL stage for exact match (#1717)
ACL table and table group attributes to identify match type (#1730)
ACL table attribute to specify Dst IPv6 valid bits (#1718)
Add an SAI_UDF_MATCH_ATTR_L4_DST_PORT_TYPE attribute to _sai_udf_match_attr_t (#1739)
Provide the ability to set Hash algorithm, offset for a port (#1775)
Fabric Switch Isolation (#1780)
WatchDog Timer Configuration for VoQ (#1779)
Add modes to update the host interface oper status. (#1646)
Update saiport.h to add new interface type for USXGMII (#1679)
A port attribute to capture debug data. (#1324)
Improve enum values integration check (#1727)
SAI-PTF Test enhancements
DASH attributes for ST routing (#1729)
DASH API (#1590)
Base ACL PR Set