## Slide 1: Adaptive Routing and Switching (ARS) in AI/ML Workloads

## Slide 2: ARS In AI/ML Workloads
Jai Kumar, Distinguished Engineer, Broadcom Inc.
Guohan Lu, Principal Engineer, Microsoft
Networking
NETWORKING

## Slide 3: Adaptive Routing and Switching
Process, where a router/switch can forward data via a different route for a given destination based on the current conditions of the communication circuits within a system
https://en.wikipedia.org/wiki/Dynamic_routing

## Slide 4: Adaptive Routing and Switching
Overview
SAI Logical Packet Flow
SAI Specification
Call for Action

## Slide 5: AI/ML Workloads
NLG (Natural Language Generation), Content understanding models
  Very large models –100s of Billions to Trillion parameters
    Example: Megatron Turning model, GPT-3
  Large distributed training–16K or 32K nodes
Recommendation models
  Deep Learning Recommendation Model (DLRM)
    Medium size – 128 to 256 nodes
    Personalized All to All communication
    Memory bound
AI/ML applications require high network utilization that keeps expensive accelerators busy

## Slide 6: Existing Forwarding Decision Model
Path selection done by routing protocols
Path selected MAY be traffic engineered
Fair available link utilization is done via
  ECMP
  LAG

## Slide 7: Challenges
Polarization
  Static Hash: No accounting for local and remote link quality
Link Failure
  Control plane interaction to rebalance the traffic
  Slow convergence
  Black holing of traffic
Static hash-based link utilization
  ECMP
  LAG

## Slide 8: Enters Adaptive Routing and Switching
Local and Remote link quality-based path selection
Past and Future link load as a quality measure
Concept of flow-let for dynamic path assignment and reassignment
  ECMP
  LAG

## Slide 9: Terms and Acronyms
Micro Flow
  A single traffic flow typically identified by 5 tuple
Macro Flow
  Collection of micro flows that hash to same value
Flow-let
  Flow-let is a contagious subsequence of packets within a macro flow
  Separated by an idle time interval
Macro Flow Table
  HW table to store per macro flow state
ARS
  Adaptive routing and switching: Path selection is influenced by various metrics

## Slide 10: Key Idea
Adaptive path assignment based on local or remote link loading state
  link load: Bytes per time interval t
  Inflight load: Queue tx byte count
  Micro flow awareness
  Load aware path assignment
  Support for minimal and non minimal cost paths
Adaptive path assignment happens for
  New macro flow assignment and reassignment
  Automatic best path reassignment for link failure or admin down state
  No ECMP path shuffling and thereby NOT impacting the other flows

## Slide 11: Key Idea…..contd
Primary and Alternate paths
  Typical ECMP group consists of equal cost active members
  ARS ECMP group members are partitioned into primary and alternate set
  Alt-path is used when primary path link quality worsens below threshold
Path selection modes
  Flow-let based
    best quality path till the flow-let hits an idle time
    random path with out considering path quality
  Per packet
    best quality path assignment for each packet
    random path assignment for each packet
  Fixed: fixed path assignment, mostly used for deb

## Slide 12: ARS Stages
Data collection for computing quality
  Sampling rate (Global)
Quality metric generation
  Algorithm decision: EWMA
  Algorithm quality parameters: instantaneous load, future load
  Quantization: Compaction of quality measured data
  Quality bands: Mapping of quantized quality to quality bands
Participating links
  Scaling factor for normalization of different port speeds
  Weight of instantaneous load and future load in quality computation
Macro Flow Table state
  Managed by switch pipeline

## Slide 13: Conceptual Packet Flow
…
…
Flow-let
X
Idle time
ECMP Group with AR
X
X
X
X
A
B
C
D
Link Quality Metrics
Packet Field Hash
Micro Flow 1
Micro Flow 2
Micro Flow 3
Macro Flow
Micro flow 1 | Next hop B | active
Micro flow 2 | Next hop D | active
Micro low 3 | Next hop B | expired
Optimal member assignment
Macro Flow Table
Macro Flow
(NHG with ARS)

## Slide 14: Logical Pipeline Flow
SAI_ARS_PROFILE_ATTR_ALGO
SAI_ARS_PROFILE_ATTR_PORT_LOAD_PAST
SAI_ARS_PROFILE_ATTR_SAMPLING_INTERVAL
SAI_ARS_PROFILE_ATTR_PORT_LOAD_FUTURE
SAI_ARS_PROFILE_ATTR_QUANT_BANDS
Macro Flow Table Update
SAI_ARS_PROFILE_ATTR_QUANT_BAND_xxx_THRESHOLD
L3 Route Lookup
NHG
ARS Macro Flow ID
NHG Member Flow ID
Micro Flow
Micro Flow
Micro Flow
Micro Flow
Macro Flow Table
VRF, DIP
Regular ECMP Processing
ARS Enabled
yes
no
Background Processing

## Slide 15: Deployment Considerations
Following traffic class is not eligible for adaptive routing
  BUM traffic– Broadcast, unknown unicast, multicast
  Mirror traffic
Eligibility Criteria
  ACL based enable/disable ARS
  Ether-Type eligibility map
  Next hop group based enable/disable ARS
Incremental Deployment
  Only certain ports are qualified to participate in ARS – Use ACL
  Only certain flows are qualified to participate in ARS – Use ACL

## Slide 16: Deployment Considerations . . . . contd
Evaluation
  Use ARS monitor
    Mirror copies when path is assigned/reassigned
  ARS Nexthop Group Counters
    Link/path utilization

## Slide 17: ARS Monitoring
Problem Statement
  Operator MAY want to know when a flow is assigned to a path
  Operator MAY want to know when a flow is re-assigned to a new path

## Slide 18: ARS Monitoring Configuration and Control
Per ECMP Group
  Enable ARS monitoring
  Assign Sampler and Mirror
Counters
  Port/member reassignment counters
  ARS Next hop group drop counters

## Slide 19: SAI Spec Enhancements

## Slide 20: Scope
L3 Forwarding
  ARS capable Nexthopgroup
  ARS capable Nexthop members and ports
  ARS with non least cost path selection
L2 Forwarding
  ARS capable LAG interfaces
ARS Algorithm with Quantization
  EWMA
Increment Deployment
  ACL based ARS enable/disable
ARS Statistics
  Path assignment/reassignment/drop statistics
  Per LAG/Nexthopgoup
ARS Monitoring
  Ability to monitor path change for a given flow

## Slide 21: SAI Object Hierarchy
Switch Object
ARS Profile Object
Next Hop Group Object
Route Entry Object
AR nexthopgroup type attributes
ARS Profile object attributes
Port Object
AR link quality type attributes
ACL Entry Object
ACL AR action type
Next Hop Object
Alternate or primary AR members
New ARS Profile Object
New ARS Object
LAG Object
New ARS Object

## Slide 22: Call to Action
Join SAI community to review the PR
https://github.com/JaiOCP/SAI/tree/JaiOCP-ars

## Slide 23: Thank you!